WORKS CONTRACT NOTICE

HUHR/1101/1.2.2/1010

Modernisation of the Őrtilos connecting road no. 68118 between sections 3+670 – 5+900 (K681.01)

Location - Somogy County/Hungary

Publication reference

HUHR/1101/1.2.2/1010 Works (K681.01)

Procedure

Local Open

Programme title

Hungary-Croatia IPA Cross-border Co-operation Programme 2007-2013

Financing

Financing agreement

Contracting Authority

Nemzeti Infrastruktúra Fejlesztő Zrt. (National Infrastructure Developing Private Company Limited)

H-1134 Budapest

Váci út 45.

Hungary

CONTRACT SPECIFICATIONS

Description of the contract

In order to facilitate bicycle traffic (in line with the planned section between Murakeresztúr and Barcs of the Tree river bicycle tour route) the strengthening and widening up to 4m of the deteriorated pavement of road no. 68118 shall be done together with the renewal of the water shafts, dewatering of the embankments and the relocation of the public utilities.

The main technical parameters:

|  | Section 1. | Section 2. |
| --- | --- | --- |
| Extent of the sections: | 3+670 - 5+634 km. | 5+634 - 5+900 km. |
| Section length: | 1964 m | 266 m |
| Nature of the road: | countryside |
| Natural circumstances: | C |
| Classification of road: | other public road |
| Design class: | K.VI. |
| Design speed: | 50 km/h |
| Pavement width: | 4,00 m (4,5 - 6,0 m in curves) |
| Crown width: | 7,00 m (7,5 - 9,0 m in curves) |

The Contractor shall obtain and cover the costs of the permits of the public utility relocations, arrange all the necessary multilateral agreements, and easements.

The available financial resources: 856.306 EUR without VAT.

Number and titles of lots

Lot1: Road renewal works of Section 1 between the 3+670 - 5+634 km sections

Lot 2: Road renewal works of Section 2 between the 5+634 - 5+900 km sections

TERMS OF PARTICIPATION

Eligibility and rules of origin

Participation is open to all legal persons [participating either individually or in a grouping (consortium) of tenderers] which are established in a Member State of the European Union or in a country or territory of the regions covered and/or authorised by the specific instruments applicable to the programme under which the contract is financed (see item 22 below). All goods supplied under this contract must originate in one or more of these countries. Participation is also open to international organisations. Participation of natural persons is directly governed by the specific instruments applicable to the programme under which the contract is financed]

Grounds for exclusion

Tenderers must submit a signed declaration, included in the Tender Form for a Works Contract, to the effect that they are not in any of the situations listed in point 2.3.3 of the Practical Guide.

Number of tenders

Tenderers may submit only one tender per lot. Tenders for parts of a lot will not be considered. Any tenderer may state in its tender that it would offer a discount in the event that its tender is accepted for more than one lot. Tenderers may not submit a tender for a variant solution in addition to their tender for the works required in the tender dossier.

Tender guarantee

No tender guarantee is required.

Performance guarantee

The successful tenderer will be asked to provide a performance guarantee of 5% of the amount of the contract at the signing of the contract. This guarantee must be provided together with the return of the countersigned contract no later than 30 days after the tenderer receives the contract signed by the Contracting Authority. If the selected tenderer fails to provide such a guarantee within this period, the contract will be void and a new contract may be drawn up and sent to the tenderer which has submitted the next cheapest compliant tender.

Information meeting and/or site visit

No information meeting is planned.

Tender validity

Tenders must remain valid for a period of 90 days after the deadline for submission of tenders.

Period of implementation of tasks

In case of both lots: The contract must be accomplished within 3 months as from the commencement order.

SELECTION AND AWARD CRITERIA

Selection criteria

1. Economic and financial capacity of candidate:

For tendering Lot 1:

(a)	The average annual turnover of the tenderer in the past three years (2011, 2012 and 2013) must exceed the amount of EUR 600,000;

For tendering Lot 2:

- The average annual turnover of the tenderer in the past three years (2011, 2012 and 2013) must exceed the amount of EUR 200,000;

For tendering both of the lots:

(a)	The average annual turnover of the tenderer in the past three years (2011, 2012 and 2013) must exceed the amount of EUR 800,000;

2. Technical and professional capacity of candidate:

For tendering Lot 1 only:

(a)	The Tenderer has completed and ended -in accordance with the prescriptions of the relevant contracts- minimum one contract in the field of construction or reconstruction of roads with the width of min. 4,0 in the total lengths of min. 1,5 km, within the period of five years before the deadline for submission of tenders. This means that the taking-over certificates of the works the tenderer refers to must have been issued within the indicated period. The criterion can be fulfilled both one or more reference contracts.

The Contracting Authority reserves the right to ask for copies of certificates of the taking over certificate / final acceptance signed by the supervisors/contracting authority of the project concerned;

(b)	The Tenderer has at least one employee with Msc or Bsc qualifications on the field of the technical sciences/engineering and with a minimum 36 month professional experience -gained after having the required qualifications- in the technical management of public road construction works including at least 1 project aiming at the construction or reconstruction of a road in the length of min. 1,5 km. The completion of the contract shall only be commenced when this project leader will have obtained the licence marked “MV-KÉ” according to the Government decree 266/2013 (VII.11.) or the “MV-KÉ/A” according to the 244/2006 (XII.) Government decree (or equivalent licence) and listed in the register of the Hungarian Chamber of Engineers as so.

(c)	The Tenderer has at least the following road construction equipment:

- 1 pieces of level controlled asphalt finisher

- 2 pieces of grader

- 2 pieces of compressing roller

- 2 pieces of loader

For tendering Lot 2 only:

(a)	The Tenderer has completed and ended -in accordance with the prescriptions of the relevant contracts- minimum one contract in the field of construction or reconstruction of roads with the width of min. 4,0 in the total lengths of min.  200 m, within the period of five years before the deadline for submission of tenders. This means that the taking-over certificates of the works the tenderer refers to must have been issued within the indicated period. The criterion can be fulfilled both one or more reference contracts.

The Contracting Authority reserves the right to ask for copies of certificates of the taking over certificate / final acceptance signed by the supervisors/contracting authority of the project concerned;

(b)	The Tenderer has at least one employee with Msc or Bsc qualifications on the field of the technical sciences/engineering and with a minimum 36 month professional experience -gained after having the required qualifications- in the technical management of public road construction works including at least 1 project aiming at the construction or reconstruction of a road in the length of min. 200 m. The completion of the contract shall only be commenced when this project leader will have obtained the licence marked “MV-KÉ” according to the Government decree 266/2013 (VII.11.) or the “MV-KÉ/A” according to the 244/2006 (XII.) Government decree (or equivalent licence) and listed in the register of the Hungarian Chamber of Engineers as so.

(c)	The Tenderer has at least the following road construction equipment:

- 1 piece of level controlled asphalt finisher

- 2 pieces of grader

- 2 pieces of compressing roller

- 2 pieces of loader

For tendering both of the Lots:

(a)	The Tenderer has completed and ended -in accordance with the prescriptions of the relevant contracts- minimum one contract in the field of construction or reconstruction of roads with the width of min. 4,0 in the total lengths of min. 1,7 km, within the period of five years before the deadline for submission of tenders. This means that the taking-over certificates of the works the tenderer refers to must have been issued within the indicated period. The criterion can be fulfilled both one or more reference contracts.

The Contracting Authority reserves the right to ask for copies of certificates of the taking over certificate / final acceptance signed by the supervisors/contracting authority of the project concerned;

(b)	The Tenderer has at least one employee with Msc or Bsc qualifications on the field of the technical sciences/engineering and with a minimum 36 month professional experience -gained after having the required qualifications- in the technical management of public road construction works including at least 1 project aiming at the construction or reconstruction of a road in the length of min. 1,7 km. The completion of the contract shall only be commenced when this project leader will have obtained the licence marked “MV-KÉ” according to the Government decree 266/2013 (VII.11.) or the “MV-KÉ/A” according to the 244/2006 (XII.) Government decree (or equivalent licence) and listed in the register of the Hungarian Chamber of Engineers as so.

(c)	The Tenderer has at least the following road construction equipment:

- 1 piece of level controlled asphalt finisher

- 2 pieces of grader

- 2 pieces of compressing roller

- 2 pieces of loader

And additionally, for tendering any Lots:

(d)	if it is a sole tenderer it must carry out at least 70 % of the contract works using its own resources, which means that it must have the equipment, materials, human and financial resources necessary to carry out that percentage of the contract.

(e)	if it is the lead member of a joint venture/consortium, it must be able to carry out at least 50 % of the contract works using its own means.

If a tender is submitted by a consortium, unless specified, the selection criteria listed above will be applied to the consortium as a whole.

An economic operator may, where appropriate and for a particular contract, rely on the capacity of other entities, regardless of the legal nature of the links which it has with them. Some examples of when it may not be considered appropriate by the Contracting Authority are when the tenderer relies mostly on the capacity of other entities or when it relies on key criteria. In the case of the present tender the reference criteria is deemed to be such criteria by the Contracting Authority, of which can not be provided by other entities. If the tenderer relies on other entities, it must prove to the Contracting Authority that it will have at its disposal the resources necessary to perform the contract, for example by producing an undertaking on the part of those entities to place resources at its disposal. Such entities, for instance the parent company of the economic operator, must respect the same rules of eligibility and notably that of nationality, as the economic operator. Furthermore, the tender should include a separate document providing data on this third entity for the relevant selection criterion. Proof of capacity must be furnished at the request of the Contracting Authority.

Award criteria

Price

TENDERING

How to obtain the tender dossier

The tender dossier is available from Sugallat Kft. (1221 Budapest, Leányka street 38. VI./39.) upon payment of HUF 5.000 (Eur 17), which excludes courier delivery. It is also available for inspection at the premises of the Sugallat Kft.. Tenders must be submitted using the standard tender form included in the tender dossier, whose format and instructions must be strictly observed.

Tenderers with questions regarding this tender should send them in writing to Sugallat Kft. Postal address: H-1221 Budapest, Leányka u. 38. Fax: +36-1-229-0113. E-mail: benko@sugallat.hu. insert specific e-mail and postal addresses (mentioning the publication reference shown in item 1) at least 21 days before the deadline for submission of tenders given in item 19. The Contracting Authority must reply to all tenderers' questions at least 11 days before the deadline for submission of tenders. Eventual clarifications or minor changes to the tender dossier will be published at the latest 11 days before the submission deadline on the Contracting Authority's website at http://www.nif.hu/hu/kozbeszerzes/prag_eljarasok/

Deadline for submission of tenders

14:00 Central European Time on 30th of June, 2014. At the premises of the Sugallat Kft. (1221 Budapest, Leányka street 38. VI./39.) Tenders may be submitted between 9:00 and 15:00. on working days, except for the day of deadline for submission of tenders when submission is possible between 9:00 and 14:00.

Any tender received after this deadline will not be considered.

Tender opening session

Time and date: 14:15 CET on 30th of June, 2014.

Venue: Sugallat Kft. (1221 Budapest, Leányka street 38. VI./39.)

Language of the procedure

All written communications for this tender procedure and contract must be in English.

Legal basis

Subsidy contract for the implementation of project No: HUHR/1101/1.2.2/1010 Works (K681.01) Légrád and Őrtilos on bike: Improving the conditions of cycling tourism in the interior of the municipalities of Légrád and Őrtilos

Council Regulation (EC) No 1085/2006 of 17.7.2006 establishing an Instrument of Pre-Accession Assistance (IPA)

Commission Regulation (EC) No 718/2007 of 12.7.2007 implementing Council Regulation (EC) No 1085/2006 of 17.7.2006 establishing an Instrument of Pre-Accession Assistance (IPA)

Practical Guide to contract procedures for EC external actions